## Slide 1: By : p pavani
Network Protocols…

## Slide 2: TCP / IP
TCP/IP is the base communication protocol of the internet.
IP , part of TCP / IP uses numeric IP addresses to identify where data is being sent.
TCP , part of TCP / IP provides reliable delivery of messages between networked computers , by splitting the message , if required .
Responsible for transmitting the data by including addressing , mapping and acknowledgement.

## Slide 3: Addressing , Mapping and Acknowledgement
Addressing : TCP on sending packets , numbers them and equips them with an address where they are to be sent , and passes them on to the IP layer for transport , i.e. for actual delivery .
Mapping : IP does its best to deliver the packets at the destination by mapping to the destination address . Destination is identified by the IP address . Sometimes , like with real post office , the packets may get lost or delayed .
Acknowledgement : Once the packet reach to the destination computer , TCP on the receiving sides takes the incoming packets , sorts them and requests re-transmission of any missing components .
Finally , the message will be delivered to the application identified by the port number .

## Slide 4: SLIP / PPP
SLIP – Serial Line Internet Protocol
For delivering IP packets over dial-up lines .
PPP – The Point-to-Point Protocol is a data link protocol commonly used in establishing a direct connection between two networking nodes and enabling IP communication over this direct connection.
IPCP -> IP Control Protocol -> for transportation over PPP link .
NCP -> Network Control Protocol -> for traffic transportation .
LCP -> Link Control Protocol -> for link establishment .

## Slide 5: SLIP / PPP Overview …
Provides the ability to transport TCP/IP traffic ever serial line( eg. Telephone lines) between